## Slide 1: Senior Design Project Summary Slide
Jesse Dengel (jad6nc@umsystem.edu)
Justin Chau (jc2w4@umsystem.edu)
Matt Mutarelli (Mnmxcd@umsystem.edu)

## Slide 2: Introduction - DAQ
DAQ – Data Acquisition System
  Measure physical signals and convert them into digital signals to view
  Oscilloscope – DAQ for specifically voltage signals
Problems with current DAQs
  Expensive
  Difficult to maintenance
  Closed system that is hard to observe
Notes: Matt

## Slide 3: COVID-19 Response Plan
COVID-19 shifts project from physical implementation to simulation demonstration tested for multiple different cases.
  Two or three weeks spent on adjusting project
  Most purchased physical components purchased became obsolete for the project demonstration
Analog section was simulated using TI TINA
  All team member are familiar with TI TINA software
  TINA comes with built in spice models for TI ICs
Notes: Matt

## Slide 4: COVID-19 Response Plan
Remove objectives for physical implementation and PCB design
  PCB designs of implementation complete, but not used
  Physical component are obsolete, but the restrictions of the components were implemented in simulation
    System Voltage from power supply
    Signal conditioning
    Microcontroller conditioning
Notes: Matt

## Slide 5: COVID-19 Response Plan
New objectives to convert analog system to circuit simulation
  Develop TINA circuits for all designed circuits
  Verify the operation of all TINA circuits through simulation
  Link TINA circuits to create simulation flow
    Export/import to transfer signals between circuits
    Excel Macro developed to format data for import
    Establish communication protocol to export data in TINA to be read in LABVIEW
  Develop demonstration videos of the DAQ system
Notes: Matt

## Slide 6: Communication Protocol
Developed and agreed upon by the analog section and the digital section to communicate the signal in the analog section to the digital section.
The signal from the analog section in TINA was exported and read by the digital system as a CSV. The first three lines contained system information about the signal and the remaining lines contained data.
Notes: Matt

## Slide 7: Analog Specifications
System Voltage: based on purchased power supply
Maximum Frequency:
Composed of multiple simple individual TINA circuit files
  Easier to comprehend each circuit in the system
  Reduced simulation time
4 Digital Input Probes:
  Regulates Voltage to logic voltages
    Logic 1: 3.3V
    Logic 0: 0V
4 Analog Input Probes:
  3 Voltage Division Options: 1:5, 1:10, 1:20
  Operates on 2 selected probes: Channel 1 and Channel 2
    Channel 1 is the primary probe
    Channel 2 is the auxiliary probe
Notes: Matt

## Slide 8: Analog Components
Linear Power Supply HBB15 – 1.5 - AG
  System Voltage DC with small ripple
  Maximum current: 1.7A
  Maximum Power : 40W
Operational Amplifier: LM318
  Used for all operational amplifier circuits
  Texas Instruments IC included in TINA
  Bandwidth: 15 MHz
Analog Multiplexer: DG408
  8:1 Analog multiplexer used for selecting signals
  Break before make switching
  Switch time: <250ns
Notes: Matt

## Slide 9: Analog Section Design Changes
Analog Input voltage Changed
  Analog Input voltage changed from to
  Reduced to match system voltage limits with 1:5 Probe
  Alternative was to increase system voltage with new power supply
FFT Equalizer Operation Removed
  The operation was designed to split the signal into multiple frequency bands to observe the different frequency components of a signal. The gain of the different bands could be changed to increase certain frequencies while attenuating other frequencies.
  The equalizer operation was removed due to time constraints due to the change in the project design and COVID-19.
  The aspects of the equalizer design were implemented in the differentiation and integration equalizers.
Notes: Matt

## Slide 10: Analog Section Design Changes
Single wide band integrator and differentiator replaced with integration and differentiation equalizer
  The frequency range from to was six decades. Using one low pass filter and one high pass filter will cause extreme attenuation.
  A system of six low pass and high pass filters that each operated on one decade of the frequency range to limit attenuation.
  Equalizer design based on removed FFT equalizer operation.
Notes: Matt

## Slide 11: Limitations of Circuit Simulation Design
Limited communication between different analog components
  No communication about what voltage division was selected
  The only communication between files was through imported/exported signals
Limited communication between analog section and digital section
  The digital section could not control the different control switches in the analog section.
  The only communication between systems was through the CSV file.
Notes: Matt

## Slide 12: Limitations of Circuit Simulation Design
Analog sampling was based on TINA simulation
  The digital section could not control the sampling of the signal in the analog section.
  TINA simulations did not generate points using a constant sampling time.
  The DAQ system assumed a constant sampling time, so the display may appeared stretched or compressed.
Notes: Matt

## Slide 13: Power Supply Circuit
Notes: Matt

## Slide 14: Block Diagram Digital Inputs
Notes: Matt

## Slide 15: Digital Input Circuit
Notes: Matt

## Slide 16: Digital Input Simulation
Notes: Matt

## Slide 17: Block Diagram – Analog Inputs
Notes: Matt

## Slide 18: Testing Process
Types of Waves
  Sine
  Triangle
Voltage Levels
  10
  20
  50
Frequencies
  1 kHz
  10 kHz
  253 kHz
Operations
  Pass
  Invert
  Addition
  Subtraction
  Differentiation
  Integration
DC

## Slide 19: Requirements
Tina
Adds data points
Exports multiple outputs in one file
Only reads tab delimited
Microcontroller
Only reads comma delimited .CSV

## Slide 20: Solutions
Macros
Separate data points
Separate data points & reduce by an order of magnitude
Add & remove necessary information for the microcontroller to use
Manual
Save as tab delimited
Save as comma delimited .CSV
Importing & Exporting

## Slide 21: The Process
Create or import signal
Run the simulation
Export as text
Import to Excel
Run required macro
Save results as correct file type
Import to Tina

## Slide 22: Analog Input Circuit
Notes: Matt

## Slide 23: Voltage Select Circuit
Notes: Matt

## Slide 24: Channel Select Circuit
Notes: Matt

## Slide 25: Pass and Invert Operations
Notes: Matt

## Slide 26: Addition Circuit
Notes: Matt

## Slide 27: Subtract Circuit
Notes: Matt

## Slide 28: Differentiation Circuit
Notes: Matt

## Slide 29: Differentiation Select Circuit
Notes: Matt

## Slide 30: Integration Circuit
Notes: Matt

## Slide 31: Integration Select Circuit
Notes: Matt

## Slide 32: Operation Select Circuit
Notes: Matt

## Slide 33: Microcontroller Conditioning Circuit
Notes: Matt

## Slide 34: SPECIFICATIONS - DIGITAL OPERATIONS
NI 6501
Uses LabVIEW to do all interactions with microcontroller
Digital Addition, Subtraction, Integration, Differentiation
Output Digital Data serially through USB
Uses NI-6501 due to COVID-19 causing restrictions on parts that are able to be ordered.
13 bit ADC at 48K samples per second
Notes: Jesse

## Slide 35: SPECIFICATIONS - DIGITAL OPERATIONS
Display Software
Use LabVIEW to receive digital data serially as a CSV data stream
Use LabVIEW to create a front panel to display results
Notes: Jesse

## Slide 36: DIGITAL OPERATIONS
Notes: Jesse

## Slide 37: SPECIFICATIONS - DIGITAL OPERATIONS
Display Software Front Panel Code
Notes: Jesse

## Slide 38: SPECIFICATIONS - DIGITAL OPERATIONS
Read CSVs and convert to an array for dislpay
Notes: Jesse

## Slide 39: Digital Operations: User Interface
Uses LabView as a basic end user interface
Installation package to works on any computer Windows 7 or above.
Ability to scale voltage and time, software performs automatically
NI-6501 can read up to 24 different channels, some channels have the option to be used as a DAC
User or calling software can select any channel to take predefined samples of channel

## Slide 40: SPECIFICATIONS - DIGITAL OPERATIONS
NI-6501
Max sampling rate
48,000 Samples
per second
Notes: Jesse

## Slide 41: SPECIFICATIONS - DIGITAL OPERATIONS
LabView DAQmx - Acquire Waveform
Notes: Jesse